# High Power LEDs MCDL-R20-300HPxx Series

## Usage Instruction

1.  Running at the maximum current of 300mA, you must use an additional heat sink board beneath the LED for cooling.

2. The operational temperature of heat sink board must be less than 55 º C to insure maximum LED life.

3.  The white, green and blue LEDs are Electrostatic Sensitive devices, So It is  important to use anti-Electrostatic protection when assembling.

# Text boxes

Heat sink board